## Slide 1: Cryogenic DRAM based Memory System for Scalable Quantum Computers: A Feasibility study
Swamit Tannu
Doug Carmean
Moinuddin Qureshi
MEMSYS-2017
Notes: Thanks sally for giving us great insights into cool memory,
Good Morning ! I am swamit, thank you for coming to my talk. I am a PhD student at Georgia Tech and this work was done in collaboration with Doug Carmean at Microsoft Research, and My advisor Moinuddin Qureshi at Georgia Tech

## Slide 2: Outline
Background: Quantum Computing
Why Cryogenic DRAM for Quantum Computers?
Experimental Setup & Challenges
Observations
Conclusion
Notes: Today, I will talk about why quantum computers will require large capacity memories at cryogenic temperature, and can I will describe how did we charchterize DRAM at cryogenic temperature as a potential memory technology for quantum computers

## Slide 3: Why Quantum Computers?
Quantum computers provide large speedup for problems in material science, machine learning, and medicine
Quantum Computers enable solutions to important problems
Execution Time
Classical Computer
Problem Size
Quantum
Computer
Molecule and Material Simulations
Billion Years
Days
Notes: Why build quantum computers?
- Can solve fundamentally hard problems material science, machine learning, and medicine
- Provide exponential speedups for problems which are currently unsolvable on conventional computers
Segway- Quantum algorithms utilize properties of quantum bits to achieve exponential speedup

## Slide 4: Qubits: Background
Quantum computer use quantum bits (qubits) to encode the information
Classical Bit
Quantum Bit
State of a Classical Bit
 1 or 0 two points on sphere
State of a Quantum Bit
Any point on the sphere
Notes: The conventional computers use bits which has binary value. If we imagine a sphere a value of a single bit can describe two points on the sphere lets say top most point and bottom most point. However, with a single qubit we can describe all the points on sphere. So the quantum computers have ability to process enormeous amounts of information than the conventional computer don’t. So quantum computer solve problems by manipulating the state of the qubit.
Segway– How do we manipulate the state of the qubit

## Slide 5: Organization of Quantum Computer
Control Processor instructions to qubits, to manipulate qubit state
Quantum Computer
Control Processor
Qubits
Notes: To manipulate the state of qubits we need a conventional computer – ‘control processor’. The control processor is an interface between qubits and the control processor.
Seems like straight forward design, so what's stopping us from building large scale quantum computer– qubits are fundamentally fickle, they can lose their state by interacting with environment
but even at small temperature

## Slide 6: Qubits are fickle
Qubits are fickle, kept at extremely low temperature (~20mK)
No quantization  small change in state lead to errors
Room temperature  too noisy to operate
1
0
Classical Bit
Quantum Bit
Notes: To manipulate the state of qubits we need a conventional computer – ‘control processor’. The control processor is an interface between qubits and the control processor.
Seems like straight forward design, so what's stopping us from building large scale quantum computer– qubits are fundamentally fickle, they can lose their state by interacting with environment
but even at small temperature

## Slide 7: Todays Quantum Computer
20mK
Dilution Refrigerator
Qubits
5 Qubit Chip (IBM)
5 Qubit Chip (IBM)
Notes: 1 min
Boarder Qubit, and Control

## Slide 8: Cryogenic Control Processor
Cryogenic Control Processor is essential for scalable Quantum Computer
(Ref: Cryogenic Control Architecture for Large-Scale Quantum Computing by Hornibrook et. al)
Control Processor
Qubits
20mK
300K
Metal Wires
 Thermal Leakage
Qubits
20mK
Control Processor
Superconducting wires
 Low Leakage
4K

## Slide 9: Memory for Quantum Computers
Quantum Computer
Control Processor
Qubits
Memory
Data Memory
Program Memory
Quantum computers require substantial memory capacity at cryo temperature
Program Memory + Data Memory  Stores Quantum Executable , Data , ECC-frames (~10s GB)
Memory must be kept at cryogenic temperature to avoid large thermal gradient
Josephson Junction technology works at 4K
 Limited memory density (only few Mb)
Notes: Monologue:

## Slide 10
Does commodity DRAM work at cryogenic temperatures ?
Goal: To characterize DRAM at cryogenic temperature to understand the functionality and error patterns
Notes: Skip THIS AND MOVE IT TO BACKUP

## Slide 11: Why Memory Fails at Cryogenic Temperature?
Temperature
Threshold Voltage
Carriers (e-)
Faults
At low temperatures, carrier freezeout can cause increase in threshold voltage
 worsens error rate
Minimum Operational Temperature (MOT) 
Minimum temperature for fault free operation
Notes: Th Voltage intu
Chuck The graph

## Slide 12: OUTLINE
Background- Quantum Computing
Why Cryogenic DRAM for Quantum Computers
Experimental Setup & Challenges
Observations
Conclusion
Notes: Goal and Outline
Goal
Setup
Challenges
Obserbations

## Slide 13
Need mechanism to reduce DIMM temperature without affecting tester
Conventional memory testing  Memtest86 running on host, dedicated memory testers
Host machines or memory testers do not work at cryogenic temperatures
How to Test DRAM at Cryogenic Temperature?

## Slide 14: Isolated Cooling of DIMM
Need cryogenic coolant  Liquid Nitrogen (boils at 77K)
Need isolated cooling of DIMMs  Compact cryogenic heatsink
DIMM is sandwiched between two heatsinks and can be cooled down to 80K
Compact heatsink with Liquid Nitrogen provides isolated cooling of a DIMM

## Slide 16: Challenges: Thermal Shock & Ice Condensation
THERMAL SHOCK
Time
Temperature (K)
300K
80K
Condensation
Limit rate of cooling & use isolation chamber to reduce condensation
Condensation
Notes: Number the challenges in the cruo testing
Need picture for Thermal Shock – cracked DRAM
Avoid Overlapping animations

## Slide 17: Experimental Methodology
Verify memory functionality by using march-tests
Fault  single bit fault in a burst
MOT  Minimum temperature at which no faults are observed
55
Number of Chips
750
Number of Vendors
5
Number of DIMMS
Notes: Title

## Slide 18: Outline
Background- Quantum Computing
Why Cryogenic DRAM for Quantum Computers
Experimental Setup & Challenges
Observations
-- At what temperature DIMM fails?
-- Chip failure rate
-- Chip capacity vs failure rate
-- Single bit vs Multibit faults
-- Transient vs permanent faults
Notes: Goal and Outline
Goal
Setup
Challenges
Obserbations

## Slide 19: Minimum Operational Temperature for DIMMs
18% DIMMs are functional below 90K
Chart: 
 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 81 | 87 | 94 | 98 | 99 | 100 | 101 | 103 | 104 | 107 | 107 | 109 | 112 | 112 | 112 | 113 | 113 | 113 | 114 | 116 | 116 | 116 | 117 | 119 | 119 | 120 | 120 | 121 | 121 | 121 | 123 | 123 | 123 | 123 | 125 | 126 | 129 | 130 | 132 | 132 | 132 | 135 | 137 | 138 | 153 | 162
Minimum Operating
Temperature (K)
DIMM Failure!
Notes: Title
Animation

## Slide 20: Chip Failures
92% of chips worked at cryogenic conditions— Pick cryogenic tolerant chips
Chart: 
| Functional Chips | Faulty Chip
Faults | 690 | 60
92%
8%

## Slide 21: Min Operational Temperature Vs Chip Capacity
Chart: 
 | 80 | 80 | 103 | 107 | 80 | 80 | 80 | 80 | 87 | 99 | 104 | 112 | 112 | 116 | 119 | 120 | 121 | 123 | 130 | 80 | 80 | 80 | 80 | 81 | 94 | 100 | 101 | 107 | 109 | 112 | 113 | 113 | 114 | 117 | 121 | 123 | 123 | 123 | 125 | 135 | 98 | 113 | 116 | 117 | 119 | 120 | 121 | 126 | 129 | 132 | 132 | 132 | 137 | 138 | 153 | 162
Minimum Operating
Temperature (K)
MOT increases with capacity; capacity of chip is correlated to technology node
256 Mb
512
Mb
1
Gb
4
Gb
2
Gb

## Slide 22: Fault Granularity
Uncorrelated faults  Conventional ECC can be effective for Cryo DRAM
Single bit errors  Uncorrelated faults
Linear codes (SECDED, BCH) are still effective
Single bit fault | 99.985%
Double bit fault | 0.015%

## Slide 23: Transient Vs Permanent Faults
Permanent faults  conventional sparing techniques can be used
Transient error  address fail once
Permanent error  address fail multiple times
Chart: DDR3
| Transient | Permanent
Faults | 0.41 | 0.59
Column1
Chart: DDR2
| Transient | Permanent
Faults | 0.36 | 0.64
Column1
Chart: DDR4
| Transient | Permanent
Faults | 0.525 | 0.47
Column1

## Slide 24: Conclusion
Quantum computers need dense memory at low temperature
Does Commodity DRAM Work at cryogenic temperature?
Experiments show  most commodity DRAM chips work at 90K
Error patterns are amenable to existing fault tolerance techniques

## Slide 25: Questions?
Want to know more about quantum computers?
Please visit my paper presentation at MICRO 2017  In 2 weeks in Boston!
Notes: Want to know more about quantum …
Thank you and I will be happy to take questions